| MNM Total | 0 | Fatal #’s | Coal Total | 2 | Fatal #’s | Total |
| --- | --- | --- | --- | --- | --- | --- |
| Underground (UG) |  |  | Underground (UG) | 2 | 1, 2 | 2 |
| Surface & Sur of UG |  |  | Surface & Sur of UG |  |  |  |
| Contractor |  |  | Contractor | 2 | 1, 2 | 2 |
| Powered Haulage |  |  | Powered Haulage | 1 | 2 | 1 |
| Non-Powered Haulage |  |  | Non-Powered Haulage |  |  |  |
| Machinery |  |  | Machinery | 1 | 1 | 1 |
| Roof, Rib, Highwall Fall |  |  | Roof, Rib, Highwall Fall |  |  |  |
| Electrical |  |  | Electrical |  |  |  |
| Slip & Fall of Persons |  |  | Slip & Fall of Person |  |  |  |
| Fall & Sliding Materials |  |  | Fall & Sliding Materials |  |  |  |
| Ignition/Exploding Gas |  |  | Ignition/Explosion/Fire |  |  |  |
| Hoisting |  |  | Hoisting |  |  |  |
| Inundation |  |  | Inundation |  |  |  |
| Exploding Vessel |  |  | Exploding Vessel |  |  |  |
| Explosive/Breaking Agent |  |  | Explosive/Breaking Agent |  |  |  |
| Maintenance/Repair Involved |  |  | Maintenance/Repair Involved |  |  |  |
| Examiner, Supervisor, Owner |  |  | Examiner, Supervisor, Owner |  |  |  |
| Other |  |  | Other |  |  |  |
| Age 0-19 |  |  | Age 0–19 |  |  |  |
| Age 20-29 |  |  | Age 20-29 |  |  |  |
| Age 30-39 |  |  | Age 30-39 |  |  |  |
| Age 40-49 |  |  | Age 40-49 |  |  |  |
| Age 50-59 |  |  | Age 50-59 | 2 | 1, 2 | 2 |
| Age 60+ |  |  | Age 60+ |  |  |  |
| Experience |  |  | Experience |  |  |  |
| Less than 1 year |  |  | Less than 1 year |  |  |  |
| 1-9 years |  |  | 1-9 years |  |  |  |
| 10-19 years |  |  | 10-19 |  |  |  |
| 20+ |  |  | 20+ | 2 | 1, 2 | 2 |
| Mine Site Experience |  |  | Mine Site Experience |  |  |  |
| Less than 1 year |  |  | Less than 1 year | 2 | 1, 2 | 2 |
| 1-9 years |  |  | 1-9 years |  |  |  |
| 10-19 |  |  | 10-19 |  |  |  |
| 20+ |  |  | 20+ |  |  |  |
| Job/Task Experience |  |  | Job/Task Experience |  |  |  |
| 0-7 days |  |  | 0-7 days | 1 | 1 | 1 |
| Less than 1 year |  |  | Less than 1 year |  |  |  |
| 1-9 years |  |  | 1-9 years |  |  |  |
| 10-19 |  |  | 10-19 |  |  |  |
| 20+ |  |  | 20+ | 1 | 2 | 1 |
| Shift Time (occurred) |  |  | Shift Time |  |  |  |
| 1st Shift (7am-3pm) |  |  | 1st Shift (7am-3pm) | 1 | 2 | 1 |
| 2nd Shift (3pm-11pm) |  |  | 2nd Shift (3pm-11pm) |  |  |  |
| 3rd Shift (11pm –7am) |  |  | 3rd Shift (11pm –7am) | 1 | 1 | 1 |
| Day of the Week: |  |  | Day of the Week: |  |  |  |
| Sunday |  |  | Sunday |  |  |  |
| Monday |  |  | Monday | 1 | 2 | 1 |
| Tuesday |  |  | Tuesday |  |  |  |
| Wednesday |  |  | Wednesday |  |  |  |
| Thursday |  |  | Thursday |  |  |  |
| Friday |  |  | Friday |  |  |  |
| Saturday |  |  | Saturday | 1 | 1 | 1 |

| 2019 - Month | MNM | Coal | Totals | Difference | Totals | 2018 - Month | MNM | Coal |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| January | 0 | 2 | 2 | +1 | 1 | January | 1 | 0 |
| February |  |  |  |  | 2 | February | 0 | 2 |
| March |  |  |  |  | 3 | March | 1 | 2 |
| April |  |  |  |  | 1 | April | 1 | 0 |
| May |  |  |  |  | 1 | May | 1 | 0 |
| June |  |  |  |  | 3 | June | 2 | 1 |
| July |  |  |  |  | 1 | July | 1 | 0 |
| August |  |  |  |  | 1 | August | 1 | 0 |
| September |  |  |  |  | 2 | September | 0 | 2 |
| October |  |  |  |  | 6 | October | 5 | 1 |
| November |  |  |  |  | 2 | November | 2 | 0 |
| December |  |  |  |  | 4 | December | 0 | 4 |
| 2019 Total: | 0 | 2 | 2 | +1 | 27 | 2018 Total: | 15 | 12 |

| Product | Fatal #’s For 2019 | 2019 Total product | 2018 Total product | 2017 Total product |
| --- | --- | --- | --- | --- |
| Alumina |  |  |  | 0 |
| Cement |  |  |  | 2 |
| Clay |  |  |  |  |
| Coal | 1-2 | 2 | 12 | 15 |
| Copper |  |  | 1 | 1 |
| Diatomaceous Earth |  |  |  | 1 |
| Dimension Stone |  |  | 1 |  |
| Gold Ore |  |  | 2 | 2 |
| Granite |  |  | 1 | 1 |
| Gypsum |  |  |  |  |
| Kaolin |  |  |  |  |
| Lead Ore |  |  | 1 |  |
| Lime |  |  | 1 |  |
| Limestone |  |  | 1 | 2 |
| Magnesite |  |  |  |  |
| Phosphate |  |  |  |  |
| Potash |  |  |  |  |
| Sand & Gravel |  |  | 6 | 3 |
| Sandstone |  |  |  |  |
| Shale |  |  |  |  |
| Silver Ore |  |  |  |  |
| Stone |  |  |  | 1 |
| Titanium |  |  |  |  |
| Traprock |  |  | 1 |  |

| State (2019) | Total | MNM | Coal | Fatal # |
| --- | --- | --- | --- | --- |
| Alabama |  |  |  |  |
| Illinois | 1 | 0 | 1 | C1 |
| Indiana |  |  |  |  |
| Iowa |  |  |  |  |
| Kentucky | 1 | 0 | 1 | C2 |
| Michigan |  |  |  |  |
| Montana |  |  |  |  |
| Nevada |  |  |  |  |
| New Mexico |  |  |  |  |
| New York |  |  |  |  |
| North Dakota |  |  |  |  |
| Pennsylvania |  |  |  |  |
| Texas |  |  |  |  |
| Virginia |  |  |  |  |
| Washington |  |  |  |  |
| West Virginia |  |  |  |  |

| Part 48 = 2 | Part 46 = 0 |
| --- | --- |
| All Coal = 2 Metal: UG = 0 SUR = 0 | Non Metal SUR# |

| Month | 2019 | 2018 | 2017 | 2016 | 2015 | 2014 | 2013 | 2012 | 2011 | 2010 | 2009 | TOTAL | AVG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| January | 2 | 1 | 2 | 3 | 5 | 1 | 3 | 2 | 1 | 4 | 3 | 27 | 2.45 |
| February |  | 2 | 3 | 1 | 1 | 5 | 5 | 3 | 3 | 0 | 4 | 27 | 2.7 |
| March |  | 3 | 3 | 3 | 5 | 2 | 3 | 5 | 2 | 1 | 2 | 29 | 2.9 |
| April |  | 1 | 0 | 2 | 0 | 6 | 3 | 2 | 2 | 33 | 4 | 53 | 5.3 |
| May |  | 1 | 2 | 2 | 4 | 6 | 1 | 5 | 1 | 6 | 3 | 31 | 3.1 |
| June |  | 3 | 3 | 4 | 3 | 6 | 3 | 2 | 4 | 6 | 5 | 39 | 3.9 |
| July |  | 1 | 4 | 2 | 2 | 2 | 4 | 4 | 2 | 3 | 2 | 26 | 2.6 |
| August |  | 2 | 2 | 1 | 4 | 3 | 3 | 2 | 3 | 4 | 1 | 25 | 2.5 |
| September |  | 1 | 3 | 3 | 2 | 3 | 3 | 5 | 4 | 1 | 4 | 29 | 2.9 |
| October |  | 6 | 4 | 1 | 0 | 3 | 5 | 1 | 6 | 6 | 3 | 35 | 3.5 |
| November |  | 2 | 0 | 0 | 0 | 6 | 5 | 4 | 4 | 3 | 2 | 26 | 2.6 |
| December |  | 4 | 2 | 3 | 3 | 3 | 4 | 1 | 4 | 5 | 2 | 31 | 3.1 |
| Total: | 2 | 27 | 28 | 25 | 29 | 46 | 42 | 36 | 36 | 72 | 35 | 378 | 3.13/mo |
|  |  |  |  |  |  |  |  |  |  | UBB |  |  |

Average over past 10 years (2009-2018) = 38 per year		Average over past 5 years (2014-2018) = 31 per year

Fatal #1 – N/A

Preliminary:

Cited Regulation:

Root Cause:

Best Practices:

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Fatal #1 – Machinery – UG	Illinois

On Saturday, January 5, 2019, at approximately 3:00 am, a 55-year-old miner with 28 years mining experience was performing outby laborer work when he received fatal injuries.  He was pinned between a pneumatically powered air lock equipment door and the concrete rib barrier located near the shaft bottom. (Experience: 5 weeks at mine site and 1 day performing the activity)

Cited Regulation:	Final Report is not currently available.

Root Cause: 	Final Report is not currently available.

Best Practices:

- Design and maintain ventilation controls, including airlock doors to provide air separation and permit travel between or within air courses or entries.

- Ensure that airlock doors are designed and maintained to prevent simultaneous opening of both sets of doors.

- Ensure miners are trained in the proper use of automatic doors and procedures to follow in the event the doors malfunction.

- Provide means to override automatic airlock doors and allow manual operation in case of an emergency.

- Keep the path of automatic doors clear of miners and equipment.

- When changes in ventilation are made, test automatic doors to ensure they operate safely under the new conditions.

- Perform thorough examinations of airlock doors to assure safe operating conditions.  When a hazardous condition is found, remove the doors from service until they are repaired.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Fatal #2 – Powered Haulage – UG	Kentucky

On Monday, January 14, 2019, a 56-year-old survey crew member with 30 years mining experience was fatally injured after he was struck by a loaded shuttle car.  The victim was measuring the mining height in an entry that was part of the travelway used by the shuttle car to access the section feeder.

Cited Regulation:	Final Report is not currently available.

Root Cause: 	Final Report is not currently available.

Best Practices:

- Before performing work in an active haulage travelway, communicate your position and intended movements to mobile equipment operators and park mobile equipment until work has been completed.

- Never assume mobile equipment operators can see you.  Always wear reflective clothing and permissible strobe lights to ensure high visibility when traveling or working where mobile equipment is operating.

- Be aware of blind spots on mobile equipment when traveling in the same areas where mobile equipment operates.

- Place visible warning and barrier devices at all entrances to areas prior to performing work in active travelways of mobile equipment.

- Operate mobile equipment at safe speeds and sound audible warnings when visibility is obstructed, making turns, reversing direction, etc.  Ensure sound levels of audible warnings are significantly higher than ambient noise.

- Ensure directional lights are on when equipment is being operated.  Maintain all lights provided on mobile equipment in proper working condition at all times.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

MSHA investigates all deaths on mine property; however, some deaths are unrelated to mining activity and are not counted in the statistics MSHA uses to assess the safety performance of the mining industry.  These deaths are termed "non-chargeable" and include homicides, suicides, deaths due to natural causes, and deaths involving trespassers.

MSHA uses a formal Fatality Review Committee to determine whether a questionable death is chargeable.  There are four (4) 2019 combined (Coal and MNM) mining accidents that are pending chargeability determination.

Coal Fatal Data (1900 – 2018) – This chart shows the number of coal miners working and the number of fatalities for each year.

MNM Fatal Data (1900 – 2018) – This chart shows the number of MNM miners working and the number of fatalities for each year.