| Safety Potpourri #1 The safety theme for Hanson Aggregates Pacific Southwest, Inc. for this year is: There is always time for safety! | Safety Potpourri #2 Before attempting any repair on a machine, it is mandatory that the machine is: Turned off The power is locked out The power switch is tagged Test the lockout at the local “on-off” switch to make sure the proper source has been locked out. | Safety Potpourri #3 Before restarting a machine, such as a conveyor belt, what are at least some of the steps you should take before restarting the machine: Check the conveyor or machine to make sure all persons are away from hazardous locations. If necessary, contact the control booth, If necessary, sound the start-up alarm Remove the lock and tag and safety restore power. |
| --- | --- | --- |

| Safety Potpourri #4 True or False, Do you have the right to examine the medical records AND exposure records of your fellow miners? False, you only have the right to look at your own medical records BUT you may examine the exposure records of any miner on the property. | Safety Potpourri #5 When speaking about using Hazardous Chemicals, what does “Blocking the route of exposure mean? This the term used to describe work practices, personal protective equipment and other methods that prevent hazardous chemicals from entering your body. | Personal Protective Equipment Know How #1 What is the hazardous component of rocks, sand and gravel? Crystalline Silica |
| --- | --- | --- |

| Personal Protective Equipment Know How #2 What disease or diseases can be caused by an over exposure to crystalline silica? Silicosis Decreased lung capacity Increased risk of Lung Cancer | Personal Protective Equipment Know How #3 Name at least 3 things you can do to prevent or reduce your risk of over exposure to dusts; Wear proper PPE Work upwind of blowing dusts Use water sprays on grinding, crushing or other equipment that creates dusts Wet material before handling or sweeping Use vacuums to clean when possible Maintain and clean equipment when it is not operating Utilize Control Booths (if your job permits it) and stay in booth as much as possible Do as much work (repairs, adjustments, painting, etc) away from dusty area such as shops areas. Wear clean clothes each day, do not wear dusty clothes the next day Make sure cabs, booths and other similar areas are kept clean and door seals are maintained. | Personal Protective Equipment Know How #4 To prevent flash burn from reflected UV radiation, it is recommended that under the welding hood, a person should do what? Wear an additional pair of safety glasses…even clear ones. |
| --- | --- | --- |

| Personal Protective Equipment Know How #5 True or False & Explain Why: Safety glasses fitted with side shields are excellent protection against blowing dust? False – safety glasses are primarily designed to protect against flying objects and not necessarily dust. Goggles work best. | On the Move - Mobile Equipment Safety #1 According to MSHA, what must I do before moving a piece of mobile equipment? Wear a seat belt Honk the horn. | On the Move - Mobile Equipment Safety #2 According to MSHA, what must I do when leaving a piece of mobile equipment – NOTE: the equipment will be unattended on a grade? Controls left in “Park” Parking Brake Set Wheels (or tracks) Chocked – OR – Wheels Turned Into Bank or Rib |
| --- | --- | --- |

| On the Move - Mobile Equipment Safety #3 According to 57.14132, on a piece of self-propelled mobile equipment, when must a backup alarm or other similar warning device be used? When the operator has an obstructed view to the rear. | On the Move - Mobile Equipment Safety #4 According to MSHA, when is it acceptable for persons to work in a raised loader bucket? In 57.14211 “Blocking Equipment In A Raised Position”, the bucket and the loader must be mechanically blocked and/or secured to prevent all movement including rolling or falling accidentally. The controls must also be secured to prevent persons from accidentally moving the equipment | On the Move - Mobile Equipment Safety #5 According to MSHA (57.14131(g), in what scenario would an operator of self-propelled mobile equipment NOT need to wear a seat belt? When the operator is using a motor grader… the grader operator may wear a harness and a safety line instead of a seat belt. |
| --- | --- | --- |

| Hot Stuff – Fire Prevention #1 Name the three parts of the “Fire Triangle” Air (oxygen) Heat Fuel | Hot Stuff – Fire Prevention #2 For what sort of fires does an extinguisher with an “A” rating used? Common Combustibles | Hot Stuff – Fire Prevention #3 Name the types of fires that an extinguisher with an “A, B & C” rating can be used? Common Combustibles Flammable Liquids Electrical Fires |
| --- | --- | --- |

| Hot Stuff – Fire Prevention #4 Name 3 things you do or can do to prevent fires at your operations. | Hot Stuff – Fire Prevention #5 What is the primary or most important reason fire extinguishers are mounted on mobile equipment? To permit the operator to escape or dismount the machine (create a path of escape) and if possible, extinguish the fire on the equipment. | Tie Breaking Question How many miners were recently trapped and then rescued at the Quecreek mine? Answer – 9 You are using a bench grinder to sharpen a cold chisel. Identify the personal protection devices you would use to protect yourself. Answer – Face Shield, Safety Glasses, Hearing Protection. DO NOT WEAR GLOVES, they can become entangled in the wheel. |
| --- | --- | --- |