| 1. | Is the vessel securely moored? |
| --- | --- |
| 2. | Is there safe access for personnel transfer? Is the gangway properly secured w/allowances for tide changes? |
| 3. | Are all personnel involved in the operation attired with appropriate personal protective equipment (PPE)? (Hardhats/safety glasses/PFD/steel toe over-the-ankle boots) |
| 4. | Who will be designated to supervise the barge operations? Name: Designation: |
| 5. | Are the “no smoking” and “no mobile phone” regulation being enforced? |
| 6. | Are all doors and hatches leading to internal compartments closed? |
| 7. | Are all compartments clean and oil-free? (Ballast water is OK) |
| 8. | Is the communication procedure established, understood and tested? |
| 9. | Has the crane been third-party inspected? |
| 10. | Does the crane have the required Certificate of Compliance (NAVFAC P-307, Appendix P) |
| 11. | Is the crane properly located on the barge as to provide a level lift? |
| 12. | If the crane is out-of-level has it been de-rated 10% for every degree out of level? |
| 13. | Does the barge crane operator have a valid & in-date operator license? |
| 14. | Has all WHE rigging gear been inspected? Is it properly labeled? |
| 15. | Is the spill kit readily available and contains an adequate supply of absorbent materials? |
| 16. | Are employees aboard the barge trained and qualified to clean up a spill using the spill kit? |
| 17. | Is the crane secured against accidental travel? |
| 18. | Is a durable load chart with legible letters and figures fixed in a location visible to the operator? |
| 19. | Is the crane manual and copies of the Operator’s Daily Checklist available in the crane cab? |
| 20. | Is there a complete inventory of all barge contents & equipment available? |
| 21. | Is the barge equipped with proper lighting for night mooring? |
| 22. | Is the crane equipped with the proper FAA approved mast light? |