DUTIES OF "CERTIFIED PERSONS"

Carefully review the following questions and select the BEST answer(s).

NOTE:  There may be more than one correct answer.

ANSWER KEY

1.	The provisions of Part 77 require that certain examinations and tests be made by a certified person.  A certified person within the meaning of these provisions is a person who:

[77.100 (b)]

- has been so certified for such purpose by the State in which the coal mine is

located.

- has been so certified by the Secretary (MSHA).

- is designated by the Operator to perform such inspections.

- All of the above.

2.		As per the provisions of Part 77, the term "active workings" is defined as:

[77.2 (a)]

- Any place in a coal mine where miners are normally required to work or

travel.

- Those areas of a coal mine where significant hazards are known to exist.

- The entire mine site, including all field and facility areas.

- Only the actual digging face or digging area where machinery and/or persons are 	working.

3.		Highwalls, banks, benches, and terrain sloping into the working areas shall be examined:

[77.1004 (a)]

- After every rain.

- After every freeze.

- After every thaw.

- Before men work in such areas

4.		Each active working area of the mine shall be examined:

[77.1712 (a)]

- By a certified person designated by the operator.

- At least once during each working shift.

- As often as necessary for safety.

- All of the above.

5.	Hazardous conditions noted as the result of the examinations listed in questions #3 and #4 must be:

[77.1712 (a)]

- Reported to the operator.

- Corrected by the operator.

- Addressed immediately.

- All of the above.

6.		Who must record the results of each examination conducted?

[77.1713 (c)]

- A certified person designated by the operator to conduct such inspections.

- The person designated by the operator as responsible for health and safety at

the mine.

- The certified/qualified person in charge of mining activities in the inspected area.

- Each certified person who conducted all or any part of the inspection.

7.		The examination report MUST include:

[77.1713 (c)]

- The date on which the examination was conducted.

- A report of the condition of the mine or area inspected.

- The nature and location of any hazardous conditions found.

- All of the above.

8.		The examination reports [Log Books] shall be kept:

[77.1713 (c)]

- In a minimum of two (2) separate areas to prevent total loss of the record.

- For at least two (2) years.

- In an area of the mine which will minimize the danger of destruction by

fire or other hazard.

- All of the above.

- What is the maximum percentage of methane allowed in surface installations?

[77.201]

- 0.5%

- 1.0%

- 1.5%

- 2.0%

- Continuous methane monitoring devices shall automatically de-energize equipment when:

[77.211-1]

- The monitor is not working properly

- Methane content reaches 2.0%

- Methane content reaches 1.0%

- Both a and b

- Continuous methane monitoring devices shall give an automatic warning signal when methane content reaches:

[77.211-1]

- 0.5%

- 1.0%

- 1.5%

- 2.0%

- Welding, Cutting or soldering may not commence or continue:

[77.1112 b]

- If the temperature is below 0 degree F

- If there is 1% or more methane present

- If a qualified person is not present

- Both b and c

- The specific gravity of oxygen makes it:

[(Sg. = 1.105) (Gas Chart)]

- Lighter than normal air

- Heavier than normal air

- The same as normal air

- None of the above

- Some of the effects of oxygen deficiency are:

[Study Guide]

- At 17% - Breathing is normally faster and deeper

- At 12.1% - Flame will not burn

- At 6% - Movement becomes convulsive; breathing stops; shortly after, the heart stops

- All of the above

15.	Openings in surface installations through which men or material may fall shall be

protected by:

[77.204]

- Railings

- Barriers

- Covers or other protective devices

- Any of the above

16.	Travel-ways and platforms where persons are required to travel or work shall be kept clear of:

[77.205 b]

- Extraneous material

- Stumbling hazards

- Slipping hazards

- All of the above

17.	Crossovers shall be provided:

[77.205 f]

- At a moving conveyor where it is crossed

- Over belt drives

- Near tail pieces

- All of the above

18.	Fixed ladders shall be anchored securely and installed to provide at least _____ inches of toe clearance.

[77.206 e]

- 2

- 3

- 4

- 5

- Fixed ladders shall project at least _____ feet above landings when handholds are not

provided.

[77.206 f]

- 2

- 3

- 4

- 5

20.	The following should be equipped with guards:

[77.400 a]

- Gears, sprockets, and chains

- Drive, head, tail, and take-up pulleys

- Flywheels, couplings, shafts, saw blades, and fan inlets

- all of the above

21.	Overhead belts shall be guarded:

[77.400 b]

- When they are less than 6 feet from the floor

- Where there is less than 24 inches of clearance between the belt and the roof

- If the whipping action from a broken belt would be hazardous to persons below

- None of the above

22.	Machinery guards may be removed when:

[77.400 d]

- Testing machinery

- Never

- Only when greasing or oiling

- Under supervision of a qualified person

23.	Peripheral hoods on stationary grinding machines shall have throat openings less than:		[77.401 a 1]

- 60 degrees

- 90 degrees

- 120 degrees

- 180 degrees

24.	When operating a grinding wheel the following must be worn:

[77.401 c]

- Gloves

- Leather apron

- Goggles or face shields

- Safety shoes

- Falling object protective structures shall be provided on equipment used in surface

coal mines	when?

[77.403 a]

- Using a rubber-tired piece of equipment

- Using a crawler-mounted piece of equipment

- It is necessary to protect the operator

- None of the above

- The following equipment used in surface coal mines shall be provided with roll-over protection:

[77.403a]

- Pickup trucks

- Rubber-tired or crawler-mounted self-propelled scrapers

- Front-end loaders, dozers, and graders

- Both b and c

- Machinery shall not be lubricated while in motion where a hazard exists, unless equipped with:

[77.404 d]

- Extended fittings or cups

- Proper gloves

- Speed reducers

- None of the above

- Drive belts shall not be shifted while in motion unless the machines are provided with:

[77.406]

- Stop switch near the belt

- Mechanical shifters

- Both a and b

- None of the above

29.	Compressors and compressed-air receivers shall be equipped with:

[77.412a]

- Automatic pressure-relief valves

- Pressure gauges

- Drain valves

- All of the above

- Connections to machines of high-pressure hose lines of 1 inch diameter or larger

shall use:

[77.412 d]

- Safety chains

- Suitable locking devices

- Either a or b

- None of the above

31.	Belt conveyors in locations where fire would create a hazard to personnel shall be provided with	switches to stop the drive pulley automatically in the event of:

[77.1107]

- Excessive slippage

- Lightening

- Overloading

- All of the above

32.	Unguarded conveyors with walkways shall be equipped with  _____________ along their full length.

[77.1607 cc]

- Emergency communications system

- Emergency stop devices

- Emergency cords

- Either b or c

- All of the above

33.	Un-enclosed transformers will be considered isolated if they are placed at least ______ feet above the ground.

[77.509 a]

- 6

- 8

- 9

- 10

34.	Un-enclosed transformers will be considered isolated if surrounded by:

[77.509 a]

- A fence 6 feet high and at least 3 feet from energized parts

- A fence 8 feet high and at least 3 feet from energized parts

- A fence 6 feet high and at least 5 feet from energized parts

- None of the above

35.	The voltage on bare signal or control wires accessible to personal contact shall not exceed

_____________ volts.

[77.515]

- 20

- 40

- 60

- 110

36.	Rubber gloves worn while handling high-voltage trailing cables shall be rated at least

_____________ volts.

[77.606-1a]

- 1,000

- 5,000

- 10,000

- 20,000

37.	Rubber gloves used to work on energized high-voltage surface lines shall be

electrically tested:

[77.704-8a1]

- Once each week

- Once each month

- Once every 3 months

- Once every 6 months

38.	Booms and masts of equipment operated on the surface of any coal mine shall not be operated within __________ feet of an energized overhead power line where the voltage is less than 69,000 volts.

[77.807-2]

- 10

- 15

- 20

- 30

39.	Circuit breakers protecting low- and medium-voltage circuits shall be tested and examined at least once each:

[77.900-1]

- Day

- Week

- Month

- Year

40.	Grounding resistors used on low and medium voltage 3 phase circuits shall be of ohmic value which limits ground fault current to no more than ______ amperes.

[77.901 b]

- 15

- 25

- 45

- 75

41.	A 125-pound multi-purpose dry powder extinguisher may be substituted for a water line for each ________ square feet of floor space in a metal, concrete block or other type of  structure built of non flammable construction.

[77.1109 b]

- 1,000

- 2,500

- 5,000

- 10,000

42.	What is the minimum distance between detonator and explosive storage magazines?

[77.1301]

- 15 feet

- 25 feet

- 40 feet

- 50 feet

43.	When flammable liquids are spilled, they should be:

[77.1103]

- Washed or diluted with water

- Burned away with a controlled fire

- Removed, controlled or confined immediately

- All of the above

44.	What equipment is required to have fire extinguishers?

[77.1109 c]

- Emergency vehicles

- Vehicles which carry work crews

- All mobile equipment

- None of the above

- The mine map shall be on a scale of not less than _____ or more than _____ feet

to the inch.

[77.1200]

- 100 or more than 300

- 100 or more than 400

- 100 or more than 500

- 200 or more than 500

- The spacing of contour lines on the mine map shall not exceed _____ foot elevation levels.

[77.1200 k]

- 10

- 15

- 25

- 50

47.	Vehicles containing explosives or detonators shall be:

[77.1302 a]

- Posted with proper warning signs

- Equipped with a siren

- Painted with red and white stripe markings

- All of the above

48.	Individuals working on or near water that presents a hazard:

[77.1710 g]

- Shall be required to know how to swim

- Shall wear a life jacket

- Shall not work alone in these areas

- All of the above

49.	Explosives magazines:

[77.1301 c 5]

- Must be cleaned once a year

- Must be bonded and grounded if constructed of metal

- Must be heated during inclement weather

- All of the above.

50.	Men shall not work between equipment and the highwall or spoil bank where the equipment may hinder escape from falls or slides except when:

[77.1006 c]

- Necessary to continue mining operations

- Special safety precautions have been taken when men are required to perform repair work between immobilized equipment and the highwall or spoil bank.

- Lubricating or fueling equipment

- Trouble shooting or repairing power cable