| MNM Total | 19 | Fatal Date | Coal Total | 10 | Fatal Date | Total 29 |
| --- | --- | --- | --- | --- | --- | --- |
| Underground (UG) | 4 | Jan7(2), Feb14, Jun20(2), Dec6 | Underground (UG) | 7 | Jan7(1), Feb28, Mar2, Mar20, Aug17, Sept1, Oct22 | 11 |
| Surface & Sur of UG | 15 | Jan26, Jan28, Mar4, Mar22, Jun17, Jun20(1), Jul21, Aug4, Sep9, Sept28, Oct1, Oct7, Oct17, Nov5, Dec16 | Surface & Sur of UG | 3 | Jan11, Jan14, Aug23 | 18 |
| Contractor | 4 | Jan28, Jun17, Jun20(1), Dec16 | Contractor | 3 | Jan14, Feb28, Aug23 | 7 |
| Powered Haulage | 4 | Jan26, Jan28, Feb14, Dec6 | Powered Haulage | 1 | Aug17 | 5 |
| Machinery | 7 | Mar4, Jun17, Jun20(2), Jul21, Aug4, Oct1, Dec16 | Machinery | 3 | Jan7(1), Feb28, Aug23 | 10 |
| Roof, Rib, Highwall Fall | 1 | Jan7(2) | Roof, Rib, Highwall Fall | 2 | Mar2, Mar20 | 3 |
| Electrical | 0 |  | Electrical | 1 | Sept1 | 1 |
| Slip & Fall of Persons | 2 | Jun20(1), Oct17 | Slip & Fall of Person | 1 | Jan14 | 3 |
| Fall & Sliding Materials | 0 |  | Fall & Sliding Materials | 1 | Jan11 | 1 |
| Handling Materials |  |  | Handling Materials |  |  |  |
| Inundation |  |  | Inundation |  |  |  |
| Drowning | 1 | Sep9 | Drowning | 1 | Oct22 | 2 |
| Other | 4 | Mar22, Sept28, Oct7, Nov5 | Other | 0 |  | 4 |
| Supervisor/Foreman/Lead Person | 1 | Aug4 | Supervisor/Foreman/Lead Person | 1 | Feb28 | 2 |
| Age |  |  | Age |  |  |  |
| Age 0-19 | 1 | Jun17 | Age 0-19 | 0 |  | 1 |
| Age 20-29 | 3 | Oct7, Nov5, Dec16 | Age 20-29 | 1 | Aug23 | 4 |
| Age 30-39 | 5 | Feb14, Mar4, Sept28, Oct1, Oct17 | Age 30-39 | 5 | Jan7(1), Jan11, Mar20, Aug17, Sept1 | 10 |
| Age 40-49 | 4 | Jan7(2), Mar22, Jul21, Dec6 | Age 40-49 | 3 | Jan14, Mar2, Oct22 | 7 |
| Age 50-59 | 4 | Jan26, Jan28, Jun20(1), Jun20(2) | Age 50-59 | 1 | Feb28 | 5 |
| Age 60+ | 2 | Aug4, Sep9 | Age 60+ | 0 |  | 2 |
| Experience |  |  | Experience |  |  |  |
| Less than 1 year | 5 | Jun17, Jun20(2), Jul21, Oct1, Oct17 | Less than 1 year | 0 |  | 5 |
| 1-9 years | 9 | Jan26, Jan28, Mar4, Mar22, Jun20(1), Sept28, Oct7, Nov5, Dec16 | 1-9 years | 2 | Jan7(1), Aug23 | 11 |
| 10-19 years | 4 | Jan7(2), Feb14, Aug4, Dec6 | 10-19 | 7 | Jan11, Jan14, Mar2, Mar20, Aug17, Sept1, Oct22 | 11 |
| 20+ | 1 | Sep9 | 20+ | 1 | Feb28 | 2 |
| Mine Site Experience |  |  | Mine Site Experience |  |  |  |
| Less than 1 year | 7 | Jan28, Mar4, Jun17, Jun20(2), Jul21, Oct1, Oct17 | Less than 1 year | 4 | Jan14, Feb28, Mar2, Sept1 | 11 |
| 1-9 years | 7 | Jan26, Mar22, Jun20(1), Sept28, Oct7, Nov5, Dec16 | 1-9 years | 6 | Jan7(1), Jan11, Mar20, Aug17, Aug23,, Oct22 | 13 |
| 10-19 | 4 | Jan7(2), Feb14, Aug4, Dec6 | 10-19 | 0 |  | 4 |
| 20+ | 1 | Sep9 | 20+ | 0 |  | 1 |
| Job/Task Experience |  |  | Job/Task Experience |  |  |  |
| Less than 1 year | 9 | Jan26, Mar4, Mar22, Jun17, Jun20(2), Jul21, Oct1, Oct17, Nov5 | Less than 1 year | 2 | Feb28, Mar2 | 11 |
| 1-9 years | 6 | Jan7(2), Jan28, Jun20(1), Sept28, Oct7, Dec16 | 1-9 years | 7 | Jan7(1), Jan14, Mar20, Aug17, Aug23, Sept1, Oct22 | 13 |
| 10-19 | 2 | Feb14, Dec6 | 10-19 | 1 | Jan11 | 3 |
| 20+ | 2 | Aug4, Sep9 | 20+ | 0 |  | 2 |
| Day of the Week: |  |  | Day of the Week: |  |  |  |
| Sunday | 0 |  | Sunday | 1 | Mar20 | 1 |
| Monday | 4 | Feb14, Jun20(1), Jun20(2), Oct17 | Monday | 1 | Feb28 | 5 |
| Tuesday | 2 | Mar22, Dec6 | Tuesday | 2 | Jan11, Aug23 | 4 |
| Wednesday | 2 | Jan26, Sept28 | Wednesday | 2 | Mar2, Aug17 | 4 |
| Thursday | 2 | Jul21, Aug4 | Thursday | 1 | Sept1 | 3 |
| Friday | 7 | Jan7(2), Jan28, Mar4, Jun17, Sep9, Oct7, Dec16 | Friday | 2 | Jan7(1), Jan14 | 9 |
| Saturday | 2 | Oct1, Nov5 | Saturday | 1 | Oct22 | 3 |

| 2022 - Month | MNM | Coal | Totals | Difference | Totals | 2021 - Month | MNM | Coal |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| January | 3 | 3 | 6 | +3 | 3 | January | 2 | 1 |
| February | 1 | 1 | 2 | -1 | 3 | February | 3 | 0 |
| March | 2 | 2 | 4 | +2 | 2 | March | 2 | 0 |
| April | 0 | 0 | 0 | -2 | 2 | April | 2 | 0 |
| May | 0 | 0 | 0 | -2 | 2 | May | 1 | 1 |
| June | 3 | 0 | 3 | -2 | 5 | June | 3 | 2 |
| July | 1 | 0 | 1 | -3 | 4 | July | 3 | 1 |
| August | 1 | 2 | 3 | 0 | 3 | August | 1 | 2 |
| September | 2 | 1 | 3 | 0 | 3 | September | 3 | 0 |
| October | 3 | 1 | 4 | +1 | 3 | October | 2 | 1 |
| November | 1 | 0 | 1 | -1 | 2 | November | 1 | 1 |
| December | 2 | 0 | 2 | -3 | 5 | December | 4 | 1 |
| 2022 Total: | 19 | 10 | 29 | -8 | 37 | 2021 Total: | 27 | 10 |

| Product | 2022 Fatal Dates | 2022Total | 2021 Total |  | State (2022) | Total | MNM | Coal | Fatal Date |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Alumina |  |  | 0 |  | Arkansas | 3 | 3 | 0 | Jan26, Jun20(1), Aug4 |
| Barium |  |  | 0 |  | Arizona | 1 | 1 | 0 | Jan28 |
| Cement | Jul21, Oct17, Nov5 | 3 | 1 |  | Georgia | 1 | 1 | 0 | Jun17 |
| Clay |  |  | 0 |  | Indiana | 1 | 0 | 1 | Jan7(1) |
| Coal | Jan7(1), Jan11, Jan14, Feb28, Mar2, Mar20, Aug17, Aug23, Sept1, Oct22 | 10 | 10 |  | Kentucky | 2 | 0 | 2 | Jan11, Mar20 |
| Copper | Jan28 | 1 | 1 |  | Missouri | 1 | 1 | 0 | Dec6 |
| Gold Ore | Feb14 | 1 | 1 |  | Nebraska |  |  |  |  |
| Granite | Jun17, Jun20(1), Oct7 | 3 | 0 |  | Nevada | 3 | 3 | 0 | Feb14, Mar4, Sept28 |
| Gypsum |  | 0 | 0 |  | New Mexico | 1 | 0 | 1 | Aug23 |
| Iron Ore |  |  | 0 |  | New York | 1 | 1 | 0 | Oct1 |
| Kaolin |  |  | 0 |  | Oklahoma | 1 | 1 | 0 | Oct17 |
| Lead Ore | Dec6 | 1 | 1 |  | Pennsylvania | 3 | 1 | 2 | Jan7(2), Mar2, Oct22 |
| Lime | Jun20(2) | 1 | 0 |  | Rhode Island | 1 | 1 | 0 | Oct7 |
| Limestone | Jan7(2) | 1 | 3 |  | South Carolina | 1 | 1 | 0 | Jul21 |
| Marble |  |  | 1 |  | Tennessee | 1 | 1 | 0 | Nov5 |
| Platinum |  |  | 2 |  | Texas | 2 | 2 |  | Sep9, Dec16 |
| Sand/ Sand & Gravel | Jan26, Mar4, Mar22, Aug4, Sep9, Sept28, Dec16 | 7 | 10 |  | Virginia | 1 | 1 | 0 | Jun20(2) |
| Sandstone |  |  | 0 |  | Wisconsin | 1 | 1 | 0 | Mar22 |
| Shale |  |  | 0 |  | West Virginia | 4 | 0 | 4 | Jan14, Feb28, Aug17, Sept1 |
| Silver Ore |  |  | 0 |  |  |  |  |  |  |
| Stone | Oct1 | 1 | 2 |  | Part 48 = 15 |  |  |  | Part 46 = 14 |
| Titanium |  |  | 0 |  | All Coal = 10 |  |  |  | Non Metal SUR = 14 |
| Traprock |  |  | 0 |  | MNM: UG = 4 |  |  |  |  |
| Zinc |  |  | 3 |  | Metal: SUR = 1 |  |  |  |  |

| Month | 2022 | 2021 | 2020 | 2019 | 2018 | 2017 | 2016 | 2015 | 2014 | 2013 | 2012 | TOTAL | AVG |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| January | 6 | 3 | 2 | 2 | 1 | 2 | 3 | 5 | 1 | 3 | 2 | 30 | 2.73 |
| February | 2 | 3 | 3 | 0 | 2 | 3 | 1 | 1 | 5 | 5 | 3 | 28 | 2.55 |
| March | 4 | 2 | 0 | 3 | 3 | 3 | 3 | 5 | 2 | 3 | 5 | 33 | 3 |
| April | 0 | 2 | 0 | 0 | 1 | 0 | 2 | 0 | 6 | 3 | 2 | 16 | 1.45 |
| May | 0 | 2 | 2 | 3 | 1 | 2 | 2 | 4 | 6 | 1 | 5 | 28 | 2.55 |
| June | 3 | 5 | 3 | 2 | 3 | 3 | 4 | 3 | 6 | 3 | 2 | 37 | 3.36 |
| July | 1 | 4 | 3 | 3 | 1 | 4 | 2 | 2 | 2 | 4 | 4 | 30 | 2.73 |
| August | 3 | 3 | 3 | 5 | 2 | 2 | 1 | 4 | 3 | 3 | 2 | 30 | 2.73 |
| September | 3 | 3 | 2 | 2 | 1 | 3 | 3 | 2 | 3 | 3 | 5 | 30 | 2.73 |
| October | 4 | 3 | 5 | 0 | 6 | 4 | 1 | 0 | 3 | 5 | 1 | 32 | 2.91 |
| November | 1 | 2 | 3 | 2 | 2 | 0 | 0 | 0 | 6 | 5 | 4 | 25 | 2.27 |
| December | 2 | 5 | 3 | 2 | 4 | 2 | 3 | 3 | 3 | 4 | 1 | 32 | 2.91 |
| Total: | 29 | 37 | 24 | 27 | 28 | 25 | 29 | 46 | 42 | 36 | 36 | 351 | 2.66/mo |

Average over past 10 years (2012-2021) = 33 per year		Average over past 5 years (2017-2021) = 29 per year

Jan 7(1)	Machinery	Indiana

MSHA Fatality #1 - On Friday, January 7, 2022, a 35-year-old continuous mining machine operator with 9 years mining experience died when he was pinned between the continuous mining machine and a coal rib.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Operate equipment from a safe location.  Stay out of “Red Zone” areas including pinch points, the CMM turning radius, and areas close to the ribs.

- Maintain proximity detection systems (PDS) in the approved operating condition.

- Perform the manufacturer’s recommended static and dynamic tests to assure the PDS is functioning properly.  Verify that the shutdown zones are at sufficient distances to stop the CMM before contacting a miner.

- Wear miner wearable components in accordance with PDS manufacturer’s recommendations, so warning lights and sounds can be seen and heard.

- Develop and implement procedures for tramming, repositioning, cable handling and moving remote controlled CMMs safely.

- Train miners on the function of PDS.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jan 7(2)	Fall of Roof	Pennsylvania

MSHA Fatality #2 - On Friday, January 7, 2022, a 49-year-old loader operator with 15 years mining experience died when an approximately 170-ton rock fell from the mine roof onto the cab of the front-end loader he was operating.  He was loading blasted material from the production area at the time of the roof fall.

Cited Regulation:	57.3360

Root Cause:

- The mine operator did not use ground support or otherwise control the roof where a geologic fault existed.

Best Practices:

- Scale the back and ribs before performing work in an area.

- Conduct examinations of the back, face, and ribs where miners work and travel.

- Install suitable ground support where conditions warrant.

- Use geologic hazard mapping to identify adverse conditions and be aware of changing ground conditions.

- Train miners to identify workplace hazards and take action to correct them.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jan 11	Falling Material	Kentucky

MSHA Fatality #3 - On Tuesday, January 11, 2022, a 32-year-old blaster with about 10 years mining experience died when a tree fell from the highwall adjacent to the mine road and struck the cab of the pickup truck that he was driving.

Cited Regulations:	77.1000 and 77.1713(a)

Root Cause:

- The mine operator did not follow their Ground Control Plan that required all trees be removed a safe distance from the top of the highwall.

- The mine operator did not conduct adequate examinations of all roadways and highwalls.

Best Practices:

- Remove all trees near the highwall edge.

- Conduct adequate examinations of all roadways and highwalls.

- Examine highwalls frequently and from as many perspectives as possible (bottom, sides, and top/crest).  Look for signs of instability such as cracks, sloughing, loose ground, and for fall of material hazards such as large trees and rocks.

- Train all miners to recognize hazardous highwall conditions.

- Conduct additional examinations as conditions warrant, especially during periods of changing weather conditions.

- Clear loose or potentially hazardous material from near the edge of highwalls and slopes, especially when persons will work or travel below.

- Develop and follow a ground control plan that addresses all potential hazards.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jan 14	Slip/Fall of Person	West Virginia

MSHA Fatality #4 - On Friday, January 14, 2022, a 44-year-old contract laborer with 13 years experience received fatal injuries when he fell 27 feet to a concrete surface.  At the time of the accident, the contractor was on a belt conveyor in a preparation plant and was working to replace a belt conveyor roller.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Establish and follow safety policies and procedures, when working at heights.

- Train miners to use fall protection when a fall hazard exists.

- Ensure fall protection is available and properly maintained.

- Provide identifiable and secure anchor points to attach lanyards and lifelines.

- Provide mobile or stationary platforms—or scaffolding—where there is a risk of falling.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jan 26	Powered Haulage	Arkansas

MSHA Fatality #5 - On Wednesday, January 26, 2022, a 54-year-old miner with 2 years experience was attempting to troubleshoot a brake issue when a dump truck rolled backwards over him.  The dump truck operator was unaware that the miner was under the truck when he released the parking brake, allowing the dump truck to roll backward.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Block machinery or equipment against hazardous motion before performing repairs or maintenance.

- Communicate with mobile equipment operators and assure they acknowledge your presence, before traveling near mobile equipment.  Do not assume that mobile equipment operators know that you are in the vicinity.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jan 28	Powered Haulage	Arizona

MSHA Fatality #6 - On Friday, January 28, 2022, a 56-year-old (contractor) concrete mixer truck driver with 3 years experience was fatally injured after losing control of his speed while descending the Northwest Ramp.  The truck subsequently overturned, coming to rest against a berm after sliding 252 feet on its side.  The crash resulted in fatal injuries to the driver and serious injuries to the passenger.

Cited Regulation:	56.14101(a)(3), 56.14100(a), 56.14131(a), 56.14100(c), and 56.9101

Root Cause:

- The contractor did not maintain braking systems in functional condition and did not remove equipment from service until defects that make continued operation hazardous were corrected.

- The contractor did not conduct adequate pre-operational examinations on mobile equipment prior to operation.

- The contractor did not ensure that miners wore seat belts.

Best Practices:

- Each shift, inspect mobile equipment before placing it into operation.  Correct defects that pose a hazard to miners.  Tag out and do not use mobile equipment until the identified hazards can be corrected.

- Train miners who are responsible for performing the examination on how to document the examination, how to correct the defects, where the completed documentation is turned in, and how records of corrections are kept.

- Ensure brakes can stop and hold mobile equipment with its typical load on the maximum grade it travels.

- Always wear and ensure miners are wearing the seat belt when operating mobile equipment.

- Maintain control of mobile equipment and drive at safe speeds.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Feb 14	Powered Haulage	Nevada

MSHA Fatality #7 - On Monday, February 14, 2022, a 34-year-old maintenance technician with 10 years experience died when the lube truck she was driving over traveled the edge of a stope and fell approximately 60 feet into the stope drift.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Provide berms, bumper blocks, safety hooks, or similar impeding devices at dumping locations where there is a hazard of over travel.

- Examine working places before work begins for conditions that may adversely affect safety and health.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Feb 28	Machinery	West Virginia

MSHA Fatality #8 - On Monday, February 28, 2022, a contract miner with 20 years experience died when he was crushed between the rib and a single boom face drill.  The victim was alongside the drill using the onboard tram lever controls because the remote control was inoperable. when the accident occurred.

Cited Regulations:	75.1725(a) and 75.512

Root Cause:

- The mine operator did not maintain the drill in safe operating condition.

- The mine operator did not conduct an electrical examination of the drill before placing it in service.

Best Practices:

- Mobile equipment shall be maintained in safe operating condition.  Immediately remove mobile equipment in unsafe condition from service.

- Always operate mobile equipment from a safe location.  Use the remote control or operate from within the operator’s compartment if available.

- Determine the proper working position to avoid pinch points and Red Zone areas.

- Train examiners on conducting a thorough electrical examination of drill.

- Train miners on the safety aspects and safe operating procedures of mobile equipment before use.  Review and discuss pinch points and Red Zone locations.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Mar 2	Fall of Roof/Rib	Pennsylvania

MSHA Fatality #9 - On Wednesday, March 2, 2022, a 44-year-old scoop operator with 15 years experience was fatally injured when an overhang along the mine rib fell striking the miner and pushing him against the canopy of a twin boom roof bolting machine.  The miner freed himself from the fall, but later died.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Remove overhangs with the continuous mining machine.

- Install support of proper length with surface area coverage, on cycle, and in a consistent pattern for the best protection against falls.

- Examine the roof, face, and ribs immediately before starting work in an area where people work and travel, including sound and vibration testing where applicable.

- Scale loose roof and ribs from a safe location.  Prevent access to hazardous areas until you take corrective measures.

- Take additional safety precautions when encountering new and changing roof and rib conditions.

- Train miners on how to identify hazardous roof and rib conditions.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Mar 4	Machinery	Nevada

MSHA Fatality #10 - On Friday, March 4, 2022, a 37-year-old bulldozer operator died when the bulldozer he was operating went over the edge of the highwall, landing upside down on the pit floor.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Dump loads at a safe distance from the edge of the highwall and then push the material over.

- Maintain control of mobile equipment while it is in operation.

- Perform ground condition and workplace examinations.

- Train miners to safely perform tasks.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Mar 20	Fall of Roof/Back	Kentucky

MSHA Fatality #11 - On Sunday, March 20, 2022, a 33-year-old miner with 13 years experience died when he was struck by a roof fall while moving a waterline outby the retreat mining section.  The intersection of the fall area was supported with five-foot fully grouted roof bolts and 10-foot cable bolts.  The roof fall was approximately 40 feet long, 18 feet wide, and five feet thick.

Cited Regulation:	75.361(a)(1) and 75.202(a)

Root Cause:

- The mine operator did not conduct a supplemental examination to identify and correct hazardous conditions prior to miners entering the #8 entry of the 3 South Mains where work was to be performed.

- The mine operator did not adequately support or otherwise control the roof where miners were required to work or travel.

Best Practices:

- Install adequate roof support where miners work.

- Conduct a visual examination of the roof, face, and ribs immediately before any work is started in an area.

- Be alert to changing roof conditions, especially during retreat mining.

- Train miners on how to identify hazardous roof and rib conditions.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Mar 22	Other: Drowning	Wisconsin

MSHA Fatality #12 - On Sunday, March 22, 2022, a 44-year-old heavy equipment operator with 6 years experience drowned after the floating pump station he was standing on capsized.  At the time of the accident, the miner was assisting a co-worker in connecting a water discharge line.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Design and use floating platforms in a manner that complies with the manufacturer’s specifications and recommendations.

- Before working on a floating platform:

  - implement safe work procedures that take into account potential hazards from rain, ice, freezing temperatures, and other environmental conditions.

  - perform adequate work place examinations, especially on floating platforms that are infrequently used.  Check parts that are subject to rust, sun damage, water damage, etc. over long periods of time.

- Wear life jackets where there is danger from falling into water.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jun 17	Machinery	Georgia

MSHA Fatality #13 - On Friday, June 17, 2022, a 16-year-old contract equipment operator with 3 weeks experience died when the compactor he was operating overturned, pinning him beneath the cab.  As the miner was backing up, the left tire went off the edge of a four-foot embankment, causing the compactor to overturn.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Wear seat belts at all times when operating equipment.

- Train miners to perform tasks safely, and to recognize potential hazards.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jun 20	Slip/Fall of Person	Arkansas

MSHA Fatality #14 - On Monday, June 20, 2022, a 57-year-old contract drill operator with 2 years experience was working outside of his drill when he fell over a 25-foot highwall.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Wear fall protection when there is a danger of falling.  Ensure fall protection has a suitable fall arrest and a secure anchorage system.

- Train miners to properly use their personal protective equipment and to recognize potential hazards from falls and to safely perform tasks.

- Provide communication systems when assigning miners to work alone.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jun 20	Machinery	Virginia

MSHA Fatality #15 - On Monday, June 20, 2022, a 50-year-old excavator operator with 9 weeks experience died when the excavator he was operating slid over an embankment and was engulfed by lime kiln dust.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Conduct workplace examinations prior to beginning work and assure hazards are corrected.

- Train miners to identify and report hazards and stay clear of potentially unstable areas.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Jul 21	Machinery	South Carolina

MSHA Fatality #16 - On Thursday, July 21, 2022, a 43-year-old miner with 47 weeks experience died after he became entangled in an auger conveyor.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Secure all conveyor covers in place during normal operation.  Keep tools, clothing, and body parts away from moving conveyors.

- De-energize, lock out, tag out, and block machinery against hazardous motion before performing repairs or maintenance.  Never perform work on a moving conveyor.

- Examine work areas and equipment.  Report defects to miners and assure defects are corrected and recorded.  Test emergency shut-off devices frequently.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Aug 4	Machinery	Arkansas

MSHA Fatality #17 - On Thursday, August 4, 2022, a 67-year-old mine manager with 14 years experience died while performing maintenance on a bulldozer.  While kneeling on the bulldozer’s track, the victim accidentally engaged the lever that put the bulldozer in reverse.  The bulldozer track moved the victim to the rear of the bulldozer where he was run over.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Operators should train miners on safe maintenance procedures:

- Turn off the engine.

- Block equipment against motion.

- Operators should ensure miners are in a safe location in relation to machine parts that can move.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Aug 17	Powered Haulage	West Virginia

MSHA Fatality #18 – On Wednesday, August 17, 2022, a 36-year-old general inside laborer with 13 years experience died when he was caught between a supply car and its coupler.  The victim was sitting on the supply car which was coupled to a locomotive parked in a track spur.  The locomotive was struck by another locomotive pulling three loaded cars into the mine.  The impact knocked the victim off the supply car, killing him.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Ensure track switches are in the proper position for your direction of travel and the latches are in contact with the rail.

- Ensure miners are in a safe location away from equipment parked in a track spur when other equipment is passing along the main rail line.

- Ensure miners communicate their location and intended movements with the dispatcher.  Repeat the switch alignment back to the dispatcher, where applicable.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Aug 18	Slip/Fall of Person	Utah

After examining the accident scene, conducting interviews, and reviewing evidence, MSHA investigators now believe the victim did not fall from the trailer as initially reported.  Surveillance video of the accident area shows the victim on top of the trailer, then there is a time delay, and then the driver is on the ground.  There are no eyewitnesses or video of the victim falling.  Additionally, the medical examiner stated that the victim did not have any bruising or broken bones to suggest that he fell, and the cause of death is natural causes.  This fatality will be referred to the Fatality Review Committee.

Aug 23	Machinery	New Mexico

MSHA Fatality #19 – On August 23, 2022, a 24-year-old contract mechanic with 3 years experience received fatal injuries while performing maintenance on the bucket (dipper) of an electric rope shovel.  A plastic block, used to prop open the dipper door, dislodged causing the dipper door to close and pin the victim against the back edge of the dipper.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Ensure miners are positioned in a safe location and away from potential pinch point areas.

- Make sure miners securely block equipment against motion before beginning maintenance or repairs.

- Ensure blocking material is substantial and installed correctly to support and stabilize the load.

- Ensure miners conduct repairs according to manufacturer’s recommendations.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Sept 1	Electrical	West Virginia

MSHA Fatality #20 – On Thursday, September 1, 2022, a 33-year-old roof bolter with 12 years experience was electrocuted when he contacted a metal hook that became energized after it penetrated the 480-volt cable that supplied electrical power to a roof bolting machine.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Ensure miners use suitable, non-conductive ropes when pulling or handling electrical cables.

- Never attach conductive parts, such as metallic hooks, to the portions of non-conductive ropes that contact electrical cables.

- Ensure miners use proper Personal Protective Equipment when handling cables, such as insulated gloves.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Sept 9	Drowning	Texas

MSHA Fatality #21 – On Friday, September 9, 2022, a 62-year-old dredge operator with 30 years experience drowned while working in a dredge pond.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Ensure a competent person conducts workplace examinations before miners begin work to identify conditions that may adversely affect safety.

- Ensure miners wear life jackets or belts where there is danger of falling into water.

- Ensure miners maintain communication when working alone.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Sept 28	Engulfment	Nevada

MSHA Fatality #22 – On Thursday, September 1, 2022, a 35-year-old miner with 3 years experience died when he was engulfed in a collapsed stockpile.  The miner was working close to the toe of the stockpile to remove material off the top of a surge tunnel’s feeder to clear a blockage.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Operators should have procedures to safely clear blockages from feeders, and train miners to stay out of areas where there is a danger of falling or sliding material.

- Equip feeders with mechanical clearing devices to prevent exposing miners to hazards of falling or sliding material.

- Ensure miners trim stockpiles to prevent hazards.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Oct 1	Machinery	New York

MSHA Fatality #23 – On Thursday, October 1, 2022, a 35-year-old miner with 47 weeks experience died while using a crane to remove a haul truck engine.  The auxiliary line broke, causing the hook and ball assembly to fall and strike the miner.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Ensure cranes have functional anti-two blocking devices to automatically shut off the crane when the rigging on the hoist line gets close to the sheave at the end of the crane boom.

- Ensure miners stay clear of suspended loads and use taglines when necessary for steadying or guiding suspended loads.

- Ensure miners conduct thorough pre-operational inspections of all machinery, equipment, and tools prior to use.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Oct 7	Other: Confined Space	Rhode Island

MSHA Fatality #24 – On Friday, October 7, 2022, a 29-year-old miner with 5 years experience was fatally injured when he was engulfed in material after he entered an air separator to clear a blockage.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Install mechanical flow-enhancing devices, such as mechanical vibratory devices, that can maintain material flow and prevent the need for miners to enter a confined space.

- Mine operators should establish procedures to clear blockages and train all miners in the procedures.

- Ensure miners wear a safety belt or harness equipped with a lifeline when entering a confined space, and that a second miner, similarly equipped, is attending the lifeline.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Oct 17	Slip and Fall of Person	Oklahoma

MSHA Fatality #25 – On Monday, October 17, 2022, a 32-year-old miner with 9 weeks experience died when he fell approximately 90 feet from the walkway outside the plant’s mill building.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Train miners to be aware of fall hazards in their workplace.

- Provide and maintain safe access to areas where miners work or travel.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Oct 22	Drowning	Pennsylvania

MSHA Fatality #26 – On Saturday, October 22, 2022, a 46-year-old mine examiner drowned in an underground sump.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Ensure miners de-energize, lock out, and tag out equipment before entering an area to perform repairs or maintenance.

- Ensure miners have communication systems available when assigned to work alone.

- Operators must conduct required examinations from safe locations to identify hazards, correct hazards, notify miners, and record hazards.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Nov 5	Other: Engulfment	Tennessee

MSHA Fatality #27 – On Saturday, November 5, 2022, a 21-year-old miner died when he was engulfed in a coal stockpile at a hydraulic cement operation.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Equip grates and feeders with mechanical clearing devices to prevent miners from being exposed to hazards of falling or sliding material.

- Ensure miners do not travel by foot on stockpiles or near the toe of stockpile slopes.

- Ensure miners can be seen, heard, or can communicate with others when working alone under hazardous conditions.

- Examine working places to identify the potential for falling or sliding materials prior to allowing access to areas in or around grates and feeders.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Dec 6	Powered Haulage	Missouri

MSHA Fatality #28 – On Tuesday, December 6, 2022, a 41-year-old charger died when the diesel tractor he was operating struck a pillar.  The miner was thrown from the tractor and crushed under the rear tire of the tractor.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices:

- Ensure miners wear seat belts when operating mobile equipment.

- Ensure miners maintain control of equipment while it is in operation.

- Train miners in the safe performance of their assigned tasks.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

Dec 16	Machinery	Texas

MSHA Fatality #29 – On Friday, December 16, 2022, a 26-year-old contract mechanic with a year experience died when the counterweight of an excavator, that he was trying to remove, fell and struck him.

Cited Regulation:	Final Report is not available.

Root Cause: 	Final Report is not available.

Best Practices: 	Fatal Alert is not available.

| Use the following links to view additional information: |
| --- |
| Preliminary Report | Fatal Alert | Final Report |

These deaths are termed "non-chargeable" and include homicides, suicides, deaths due to natural causes, and deaths involving trespassers.

MSHA uses a formal Fatality Review Committee to determine whether a questionable death is chargeable.  Currently, there is one (1) 2022 mining accident pending chargeability determination.

The following are various links to Safety Training Materials on MSHA’s website.

- Toolbox Safety Talks:  https://arlweb.msha.gov/epd/efsms/toolbox/

- Mobile Equipment Safety:  https://www.msha.gov/training-education/safety-and-health-materials/safety-topic-mobile-equipment-surface-mines

- Conveyor Systems:  https://www.msha.gov/training-education/safety-and-health-materials/safety-topic-conveyor-systems

- Impoundments and Dams:  https://www.msha.gov/training-education/safety-and-health-materials/safety-topic-impoundments-and-dams

- Seat Belts:  https://www.msha.gov/training-education/safety-and-health-materials/safety-topic-seat-belt-usage

- Guarding:  https://www.msha.gov/guarding-slide-presentation-guarding-conveyor-belts-metal-and-nonmetal-mines

- Training Videos:  https://www.msha.gov/msha-training-videos

- Another very helpful item is MSHA’s Data Retrieval System.  With your Mine ID number, you can research the violation history and accident history of the mine.  This is great site-specific information to use during annual refresher.  When you type in the ID number, it will pop up a suggestion; always click on the suggestion instead of clicking enter.  https://www.msha.gov/mine-data-retrieval-system