| Category | Sub-Category | Title | Made By | Phone # | Video ID | Date Rec'd | Play, min |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Equipment | Mobile | Visibility & Communications: Off-Road and Highway Trucks | MSHA | 304-256-3257 | VC869 | 1996 | 16 |

QUESTIONS

- No-one should approach a haulage truck without first: a) flashing your lights, b) hitting your brakes, c) making eye contact with the driver and getting the operator’s OK, d) honking their horn, e) stopping first.

- Larger trucks have: a) larger blind areas around them, b) smaller blind areas around them.

- The driver of a typical 150 ton haul truck can’t see a 6 foot tall person who is up to ____ feet from the right side of the truck: a) 10, b) 30 , c) 50, d) 70, e) 90.

- The driver of a typical 150 ton haul truck can’t see a 6 foot tall person who is up to ____ feet from the front of the truck: 20, 40, 60, 80.

- Special optical systems are needed to see a person standing directly behind a haul truck. T__, F__

- Pulling into and parking in the blind area of a haulage truck is always dangerous. T__, F__

- Conditions that improve vehicle operator awareness of the presence of other vehicles include: a) repetitious use of a haul road, b) plenty of sleep, c) staying away from alcohol and drugs, d) b and c are correct, e) a, b, and c are  correct

- Always back perpendicular to the dump. T__, F__

- Always use the berm to stop you to save wear on your trucks brakes. T__, F__

- Never back up if you can’t see the berm: T__, F__

- In bad weather, consideration should be given to stopping haulage operations. T__, F__

- Haul roads should: a) be designed to minimize blind areas, b) have speed limits that make it possible for drivers to stop within their sight distances, c) have traffic control signs that can be understood by all drivers using the roads, d) a-c are correct, e) b and c only are correct.

- Additional lights installed on trucks: a) only create an additional hazard, b) are sometimes needed.

- Stationary convex mirrors a) are used to provide visibility around blind corners, b) distort depth perception, c) are best used in combination with flat mirrors, d) a-c are correct, e) a and c only are correct.

- Video cameras which allow the operator to see in areas where mirrors can’t are coming into use at mining operations. T__, F__

- A disadvantage of back-up alarms is that: a) they can’t be heard, b) workers hear them too much to pay attention, c) they don’t help the driver know what is behind, d) a-c are correct, e) a is not correct.

- A discriminating backup alarm system: a) only beeps outside when there is something behind, b) beeps outside when starting backing up, and then only when it detects something or someone behind the truck, c) beeps inside the operator’s compartment letting the operator know the alarm system is working, d) may let the operator know when there is something or someone behind, e) b-d are correct.

- Radio or mobile telephone communications are useful tools in the prevention of vehicle accidents. T__, F__

- A haul-truck operator should sound the horn: a) before starting the engine, b) before moving any part of the vehicle, c) both a and b are correct.

- Which are true? Signs must be: a) legible, b) well-maintained, c) up to date, d) understandable by all who use the roads, e) have at least 1-inch high letters, f) tell the whole story g) be legible from 150 yards, h) e-g are incorrect, i) a-c only are correct.

| Category | Sub-Category | Title | Made By | Phone # | Video ID | Date Rec'd | Play, min |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Equipment | Mobile | Visibility & Communications: Off-Road and Highway Trucks | MSHA | 304-256-3257 | VC869 | 1996 | 16 |

ANSWERS

- No-one should approach a haulage truck without first: a) flashing your lights, b) hitting your brakes, c) making eye contact with the driver and getting the operator’s OK, d) honking their horn, e) stopping first.

- Larger trucks have: a) larger blind areas around them, b) smaller blind areas around them.

- The driver of a typical 150 ton haul truck can’t see a 6 foot tall person who is up to ____ feet from the right side of the truck: a) 10, b) 30 , c) 50, d) 70, e) 90.

- The driver of a typical 150 ton haul truck can’t see a 6 foot tall person who is up to ____ feet from the front of the truck: 20, 40, 60, 80.

- Special optical systems are needed to see a person standing directly behind a haul truck. T__, F__

- Pulling into and parking in the blind area of a haulage truck is always dangerous. T__, F__

- Conditions that improve vehicle operator awareness of the presence of other vehicles include: a) repetitious use of a haul road, b) plenty of sleep, c) staying away from alcohol and drugs, d) b and c are correct, e) a, b, and c are  correct

- Always back perpendicular to the dump. T__, F__

- Always use the berm to stop you to save wear on your trucks brakes. T__, F__

- Never back up if you can’t see the berm: T__, F__

- In bad weather, consideration should be given to stopping haulage operations. T__, F__

- Haul roads should: a) be designed to minimize blind areas, b) have speed limits that make it possible for drivers to stop within their sight distances, c) have traffic control signs that can be understood by all drivers using the roads, d) a-c are correct, e) b and c only are correct.

- Additional lights installed on trucks: a) only create an additional hazard, b) are sometimes needed.

- Stationary convex mirrors a) are used to provide visibility around blind corners, b) distort depth perception, c) are best used in combination with flat mirrors, d) a-c are correct, e) a and c only are correct.

- Video cameras which allow the operator to see in areas where mirrors can’t are coming into use at mining operations. T__, F__

- A disadvantage of back-up alarms is that: a) they can’t be heard, b) workers hear them too much to pay attention, c) they don’t help the driver know what is behind, d) a-c are correct, e) a is not correct.

- A discriminating backup alarm system: a) only beeps outside when there is something behind, b) beeps outside when starting backing up, and then only when it detects something or someone behind the truck, c) beeps inside the operator’s compartment letting the operator know the alarm system is working, d) may let the operator know when there is something or someone behind, e) b-d are correct.

- Radio or mobile telephone communications are useful tools in the prevention of vehicle accidents. T__, F__

- A haul-truck operator should sound the horn: a) before starting the engine, b) before moving any part of the vehicle, c) both a and b are correct.

- Which are true? Signs must be: a) legible, b) well-maintained, c) up to date, d) understandable by all who use the roads, e) have at least 1-inch high letters, f) tell the whole story g) be legible from 150 yards, h) e-g are incorrect, i) a-c only are correct.